## Slide 1: Chapter 15: The Building Blocks of Matter: The Atom and Its Nucleus Chapter 16: Nuclear Power: Fission
PHYS305
Exam Dec.2, study guide posted

## Slide 2: Atoms, nuclei: Motivation
 | World | US
Nuclear Power | 6.6% | 8%
Hydroelectric | 8% | 2.8%
Nuclear power has a much smaller carbon footprint than burning fossil fuels.
Some of the world’s and the US’s energy budget already comes from nuclear power.
The French generate nearly 80% of their electricity from nuclear fission.
While uranium is not a renewable resource, the possibility of nuclear fusion reactors in the future provides the prospect of a nearly limitless supply of fuel.

## Slide 3: What is matter made of?
Ancient Greeks: all matter made of
  Wind
  Water
  Earth
  Fire
Medieval alchemists  Enlightenment chemists (18 to 19th century after the French )
  Are chemical materials made up of common building blocks?

## Slide 4: Molecules
Smallest pieces into which you can break some compound without losing its chemical, physical properties.
  Table salt: NaCl is not toxic, even though Na and Cl are both highly reactive by themselves.
Can be broken into smaller bits: chemical elements.
Ingredients are in fixed ratios:
  Caffeine: C8H10N4O2
  Theobromine: is a bitter alkaloid of the cacao plant : C7H8N4O2

## Slide 5: The atom
“Atom” from the Greek atomos, meaning indivisible.
A number of electrons circle a nucleus containing an equal number of protons.
Nucleus contains positively charged protons and neutrally charged neutrons.
Image: http://www.ei.lehigh.edu/learners/energy/electricity/atom.gif
Cartoon: http://www.offthemarkcartoons.com/cartoons/2004-02-25.gif
Z electrons: charge -Ze
N neutrons: no charge
Z protons: charge +Ze
Total nucleons: N +Z = A

## Slide 6: The atom, in numbers
Size of atom: calculated: 10-10m ( Å = Angstrom)
Size of nucleus: 10-15m (fm = femtometer = fermi)
Z = ATOMIC NUMBER
= number of protons
= number of electrons unless ionized.
N = NEUTRON NUMBER
A = ATOMIC MASS
= number of nucleons = Z + N
A particular nucleus is labeled as AX, where A = atomic mass, X is the symbol in the Periodic Table for that element, which tells us what Z is.

## Slide 7: Ions
If an atom loses or gains an electron or more, it becomes charged, and is called an “ion”. Its element doesn’t change, because it retains all its Z protons.
Much of chemistry is about how atoms in a molecule share their electrons.
Images: http://www.bbc.co.uk/schools/gcsebitesize/science/images/diag_sodium_chloride.gif
http://www.bbc.co.uk/schools/gcsebitesize/science/images/diag_calcium_chloride.gif

## Slide 8: Isotopes
Two nuclei of the same element (same Z) with a different number of neutrons (different N) are called ISOTOPES.
They behave the same chemically because they have the same number of electrons.
They have different atomic weights, A.
Some isotopes of the same element are unstable, decay.
Image: http://education.jlab.org/glossary/isotope.gif
Unstable
Stable
1H, 2H, 3H

## Slide 9: Radioactive Decay
Radioactive decay, also known as nuclear decay or radioactivity, is the process by which a nucleus of an unstable atom loses energy by emitting particles of ionizing radiation.
A material that spontaneously emits this kind of radiation—which includes the emission of energetic alpha particles, beta particles, and gamma rays—is considered radioactive.

## Slide 10: Nuclear reactions
A nuclear reaction (nuclear decay, or two nuclei exchanging nucleons, etc.) can occur only if the following are conserved:
Total charge, Z
  Electron: Z=-1
  Proton: Z=+1
  Neutron: Z=0
Atomic mass, A
  Electron: Z=0
  Proton: Z=+1
  Neutron: Z=+1
Mass + Energy/c2
Image: http://upload.wikimedia.org/wikipedia/commons/thumb/5/57/Li6-D_Reaction.svg/300px-Li6-D_Reaction.svg.png

## Slide 11: Worked problems
Consider the following nuclear reaction:
where AX is some unknown element, X, of atomic mass, A. What is this reaction element?
Uranium has an atomic number of Z=92 (See Periodic Table). A neutron has an atomic number of Z=0, but atomic mass of A=1, so
So AX is 239U.

## Slide 12: Worked problems
Consider if the previous reaction emitted an electron:
What is this reaction element?
An electron has a negative charge, so emitting an electron turns one neutron into a proton. The result is no longer has an atomic number of Z=92 (See Periodic Table). A neutron has an atomic number of Z=0, but atomic mass of A=1, so
And so AX is 239Np.

## Slide 13: Study questions
It is appropriate to think of a nucleus as a bound state of __________ held together by ______________forces.
Electrons, electric
Atoms, atomic
Molecules, molecular
Nucleons, nuclear
Protons and neutrons, electric

## Slide 14: Worked problems
Balance the following nuclear reactions:
Ra = radium, Rn = radon, both are radioactive.

## Slide 15: Einstein: Mass and energy equivalence
Einstein was the first scientist to propose the E = mc2 formula and the first to interpret mass–energy equivalence,
where c = 3.00x108m/s (speed of light in a vacuum)
Mass is just another form of energy (just like heat).
In nuclear reactions, mass can be converted to energy, and vice versa.
Image: http://1.bp.blogspot.com/-Hw_jSCNtSBA/TaRVNGi-DII/AAAAAAAAAMU/HKqGxW2diuU/s1600/einstein_e_mc2formula.jpg

## Slide 16: Mass  Energy
So, in a reaction that produces energy,
In other words, if....
Atomic mass units: u = 931.5MeV/c2= =1.660538921 kg

## Slide 17: Nuclear reaction example
Given the reaction, What is the missing result? Is energy liberated? How much?
Balancing Z & A on both sides gives us
Now balance the mass:
  Total rest mass on left side = 6.015 + 2.014 = 8.029 u
  Total rest mass on right side = 2 × 4.0026 = 8.0052 u
  Missing rest mass = 8.029 – 8.0052 = 0.0238 atomic mass units.
E=mc2:
Example from http://en.wikipedia.org/wiki/Nuclear_reaction

## Slide 18: Mass  Energy
Binding energy (B.E): Nuclei are stable because it requires energy to pull them apart into individual electrons, neutrons, and protons.
So, the whole is less than the sum of its parts
A good measure of stability is the Binding Energy per nucleon (neutron or proton).
  in other words, how hard is it to knock it apart?

## Slide 19: Fission
Nuclear fission is the process in which the nucleus of a particle splits into smaller parts (lighter nuclei).
Fission is a form of nuclear transmutation because the resulting fragments are not the same element as the original atom.
Fission as encountered in the modern world is usually a deliberately produced man-made nuclear reaction induced by a neutron.

## Slide 20: Binding energy and fission
Lightest elements
  More loosely bound than iron.
  “Fusing” them together  greater stability, releases energy
Heaviest elements
  More loosely bound than iron.
  “Fissioning” them (breaking them up)  greater stability, releases energy
  Image: http://web.njit.edu/~gary/202/assets/binding_energy.jpg
Iron is the most stable element in the universe. The heavier elements were forged in stars in processes that absorbed energy (cooled) while making them.

## Slide 21: Why isn’t atomic mass a whole number?
The Periodic Table averages over several isotopes.
(A = 1.008 for hydrogen, on average)
Neutrons and protons are almost the same mass, but not quite.
Individual isotopes have non-integer masses because of the effects of binding energy. (E=mc2 again)
Image: http://en.wikipedia.org/wiki/Isotopes_of_hydrogen

## Slide 22: Radioactivity
Unstable nucleus can decay into a more stable nucleus by emitting material.
  More stable  Greater binding energy  Less mass than started with  Energy is also emitted.
Decay is random, statistical.
  Cannot be predicted for an individual nucleus.
  Can be characterized by HALF-LIFE, time required for half the unstable nuclei to decay.

## Slide 23: Radioactive Decay
 - Alpha Decay
Emission of a helium nucleus,
Blocked by paper
 - Beta Decay
Emission of electrons e-
or positrons e+
or capture of e-
Blocked by thin foil
 - Gamma Decay
Emission of EM wave
Blocked by concrete, lead
Neutrons
  Stable inside the nucleus
  Decay in about 15 minutes outside
  the nucleus
Paper
Aluminum
Concrete, lead, etc.

## Slide 24: Radioactivity applications: the smoke detector
Alpha particles from 241Am ionize the air, allowing for current to flow in circuit.
Smoke stops the alpha particles, shuts off current.
Images: http://upload.wikimedia.org/wikipedia/commons/thumb/2/23/InsideSmokeDetector.jpg/200px-InsideSmokeDetector.jpg , http://nasdonline.org/static_content/documents/247/as235f1.gif. Accessed 11/2/11.

## Slide 25: Radioactivity units
Decay rate:
  Becquerel [Bq] = 1 event/sec.
  Curie [Ci=3.71010Bq]
    Microcurie = 10-6Ci
    Nanocurie = 10-9Ci
    Picocurie = 10-12Ci.
    Typical smoke detector: 1Ci = 37kBq
None of these measure the effect of radiation on human tissue. We’ll look at that later.

## Slide 26: Radioactive half-life
Radioactive decay is often described in terms of half-life T1/2
Half of the nuclei decay
Identical nuclides do not decay at the same half-life time.

## Slide 27: Radioactive half-life
Number of undecayed nuclei, N, falls exponentially with time.
  Half-life is to exponential decay what Doubling Time is to exponential growth.
  In theory, N never reaches zero.
  In practice, N < 1 is as good as zero. (N is a whole number!) Five half-lifes is relatively safe.
Images: http://hyperphysics.phy-astr.gsu.edu/hbase/nuclear/imgnuc/hlcurv.gif
http://www.chem.umass.edu/genchem/whelan/class_images/110_Half_Lives.gif

## Slide 28: Study questions
At 9am on Monday a radioactive sample contained four million nuclei. At 9am on Friday three million of these nuclei had decayed. The half-life of this sample is
5 days
4 days
3 days
2 days
1 day
Image: http://blogs.miaminewtimes.com/riptide/simpson.jpg. Accessed 11/9/11.

## Slide 29: Study questions
At 9am on Monday a radioactive sample contained four million nuclei. At 9am on Friday three million of these nuclei had decayed. Twenty days after the original Monday, about how many radioactive nuclei are left?
none
< 100
4000
¼ million
Image: http://wellnessuncovered.com/joomla/images/stories/simpson_fish.jpg. Accessed 11/9/11.

## Slide 30: Nuclear energy: motivation
Nuclear fission provides 6% of world’s energy production.
13-14% of world’s electricity.
France and Japan: about half of the total world nuclear production.
Same physics used in nuclear bombs
Nuclear fusion technology powers the Sun.
  could be safer, more sustainable, but presently unfeasible.
Data: http://en.wikipedia.org/wiki/Nuclear_power

## Slide 31: Nuclear power
Pros
Very compact energy/mass (ca. million times better than chemical reactions.)
No greenhouse gases generated (Co, CO2 or SO2 )*.
Reliable - Nuclear power plants have very high capacity factors, much higher than solar or wind
Cheap?
*Except for the mining, refining, transportation, etc.
Cons
Waste: both toxic and radioactive.
High cost to build and license, large initial investment for long term pay back
Security concerns, proliferation and terrorism.
Safety
  Three Mile Island (1979)
  Chernobyl (1986)
  Fukushima Daiichi (2011)
Image: http://images.wikia.com/simpsons/images/9/90/Snpp-1-.gif

## Slide 32: Nuclear fission
Nucleus (235U, 239Pu) absorbs neutron, becomes more unstable, splits into roughly equal halves, with excess neutrons and a lot of energy emitted as well.
The amount of free energy contained in nuclear fuel is millions of times the amount of free energy contained in a similar mass of chemical fuel such as gasoline, making nuclear fission a very dense source of energy.
Imagehttp://whyfiles.org/130nukes/images/fission.jpg

## Slide 33: The nuclear drop model
After absorbing a neutron, the newly unstable nucleus splits in two, like water droplet.
  Resulting nuclei tend to be unequal in mass.
  Results are random for each nucleus, but can be predicted statistically.
Image: http://www.kutl.kyushu-u.ac.jp/seminar/MicroWorld3_E/3Part3_E/3P33_E/liquid_drop_E.jpg

## Slide 34: Fission byproducts
“Droplet” breaks apart, forms two nuclei of unequal mass, plus additional neutrons.
  Several hundreds of possible isotopes produced, many toxic, most radioactive.
  Neutrons absorbed by other nuclei

## Slide 35: Nuclear chain reaction
A slow neutron can induce 235U (239Pu) nucleus to split.
Fission produces more neutrons that can cause further fissions.
  They must be slow neutrons.
  Requires 2+ neutrons to maintain.
  Reactor: close to 1 neutron/nuke for stability.
  Bomb: as many neutrons as possible.
Population analogy: How many kids must each couple produce to keep humanity alive? What happens if they produce more?
Image: http://www.daviddarling.info/images/fission.gif

## Slide 36: Chain reactions
http://www.youtube.com/watch?v=Pmy5fivI_4U&feature=related
A physics experiment where it simulates nuclear fission.
100 mousetraps with 100 balls are set off in an enclosed area by one ball.

## Slide 37: Uranium isotopes
235U: Can absorb slow neutrons, which leads to fission.
  0.7% of all uranium found in nature on Earth.
  700 million year half-life.
238U: Can absorb fast neutrons, but unsuitable for use as fissile fuel.
    99.3% of all uranium found in nature.
    4.5 billion year half-life.
Is 235U becoming a greater or smaller fraction of Earth’s uranium?
Image: uranium metal. http://upload.wikimedia.org/wikipedia/commons/thumb/d/d8/HEUraniumC.jpg/250px-HEUraniumC.jpg

## Slide 38: Uranium isotopes
 | 235U / total
Nature | 0.7%
Reactor | 3-5%
Bomb | 95%
Plutonium (239Pu) (shown on the right above) can be substituted for 235U, particularly in bombs. The only problem is that it is 100% manmade.
Because it is best suited for bomb making, keeping plutonium out of unsuitable hands is a major security issue.
Half-life = 24,000yr.
Image: http://en.wikipedia.org/wiki/File:Plutonium3.jpg

## Slide 39: How to produce fissile material
235U:
  Mined uranium is “enriched” in centrifuges by discarding some of the 238U, a slow, expensive process.
  Keeping centrifuges out of wrong hands is a major security issue.
239Pu:
  Bombard 238U with neutrons in a reactor.
  Requires nuclear industry in country of production.
Image: http://en.wikipedia.org/wiki/File:U2_-_How_to_Dismantle_an_Atomic_Bomb_(Album_Cover).png

## Slide 40: Oklo
Depleted uranium (DU; also referred to in the past as Q-metal, depletalloy or D-38) is uranium with a lower content of the fissile isotope U-235 than natural uranium.
1972: discovery of “depleted” uranium in mine at Oklo, in Gabon, West Africa: 235U/238U ratio was lower than normal.
Conclusion: 1.8 Billion years ago, natural ratio of 235U/238U ratio was 3%, not 0.7%.
  Allowed for natural sustained nuclear reaction, depleting 235U.
  Required flowing water to moderate (slow down) the neutrons.
Image: http://www.bibliotecapleyades.net/imagenes_misterios/a_mapglass2.jpg

## Slide 41: Study questions
Textbooks often depict the fissioning of 235U as n + 235U --> Kr + Ba + 3n + energy, where Kr and Ba stand for [isotopes of] krypton and barium. In reality,
this is indeed the only possible reaction that could occur.
there are many other possible reactions producing products different from Kr and Ba.
this reaction is used because it is the only one producing radioactive products.
this reaction is used because it is the only one liberating energy.
this reaction is used because Kr and Ba are the only radioactive products of environmental concern.

## Slide 42: Worked problems
Nearly two billion years ago in the Oklo region of Gabon, West Africa, it was possible for a self-sustaining nuclear reaction to take place in nature because 235U constituted about 3% of all uranium.
(a) If the half lives of 238U and 235U are 4.5 and 0.7 billion years, respectively, How many half-lifes have gone by?
(b) What about the 238U? How many half-lifes have gone by?
So probably between 50% and 100%.

## Slide 43: Nuclear power’s carbon footprint versus other electric power plants
Scrubbed coal: 960g CO2equivalent emissions/kWh (e/kW.h)
Natural gas: 443g CO2e/kWh
Nuclear power: 66g CO2e/kWh
Photovoltaics: 33g CO2e/kWh
Onshore wind farms: 10g CO2e/kWh
Sovacool, B. Energy Policy 36, 2950–2963 (2008), as quoted in http://www.nature.com/climate/2008/0810/full/climate.2008.99.html#B2
more biased, non-quantitative argument: http://www.energybulletin.net/node/15345

## Slide 44: Where does my electricity come from?
Image: http://www.eei.org/ourissues/ElectricityGeneration/FuelDiversity/Documents/diversity_map.pdf

## Slide 45: Chain reactions
Chain reaction:
  Exponentially increasing number of fissions at each stage
Nuclear bomb: uncontrolled chain reaction desirable.
  95% 235U.
Nuclear reactor: uncontrolled chain reaction is the last thing you want.
  Fissible fuel is only 3% fissionable 235U.
  Control rods allow fine control: each fission triggers only one more fission.
Image: http://www.dreamstime.com/nuclear-chain-reaction-thumb18968782.jpg

## Slide 46: Fission: chain reaction
each reaction produces ~2.5 neutrons
Each neutron can cause a new reaction
Critical: each reaction produces one reaction
SUB-Critical: each reaction produces less than one reaction
SUPER-Critical: each reaction produces more than one reaction
BOOM
Dies out
Notes: 46

## Slide 47: Uranium: enriched & depleted
Enriched uranium: contains higher fraction of fissionable 235U than occurs naturally.
  Requires artificial (human) process.
  All uranium fuel must be enriched.
Depleted uranium: contains lower fraction of fissionable 235U than occurs naturally.
  Byproduct of enrichment process
  High density, 19.1x water, denser than lead
  Various military applications: armor plating, armor piercing
  Less radioactive (and emits alphas) than naturally occurring uranium.
  Health aspects still under study

## Slide 48: Gas centrifuge uranium enrichment
Enrichment of uranium to 3% of 235U is through gaseous diffusion
Uranium oxide is treated with hydrogen fluoride and converted to UF6, which is a gas at 56.5C.
Spun at very high speeds, heavier 238U traveling to outside.
Huge banks of centrifuges needed to enrich uranium from 0.7% to 3% or higher.
Recent developments use laser enrichment by using subtle differences in the electronic structures of the atoms of the different isotopes.
Images: http://chemcases.com/images/nc-07_clip_image001_0000.jpg

## Slide 49: Coolant, moderator, control rod
Coolant: used to remove heat generated by fission, used in same way as heat generated by coal furnace to produce electricity.
  Water plays similar rule: coolant that transfers heat from fuel to produce steam to run ‘heat engine’.
Moderators: a neutron moderator is a medium that reduces the speed of fast neutrons thereby turning them into thermal neutrons capable of sustaining a nuclear chain reaction involving uranium-235.
  Fast neutrons from fission need to be slowed (but not absorbed!) to allow 235U to absorb them.
  Moderator = light atoms that absorb much of the neutrons’ energy: Graphite, heavy water, light water.
Control rods absorb neutrons to slow down reaction rate.
  Materials that absorb neutrons: Boron, Silver, Indium, Cadmium.

## Slide 50: Fission Reactor
Control rods absorb neutrons
Moderators slow the chain reaction

## Slide 51: Containment structure
Fission generates a lot of heat, this why we need cooling.
However, heat engine fluid (water/steam) can be contaminated by exposure to the neutrons, and must be contained rather than released to environment.
Redundancy designed into system to further minimize the disastrous consequences of leakage.
Image: http://library.thinkquest.org/17940/texts/images/pwrschematic.jpg

## Slide 52: Nuclear meltdown
Image: http://resources2.news.com.au/images/2011/03/14/1226021/213998-nuclear-power-plant-meltdown-2.jpg

## Slide 53: Nuclear accidents
Benjamin K. Sovacool Director of the Danish Center for Energy Technology: has reported 99 accidents at nuclear power plants, worldwide.
  57 since Chernobyl (1986).
  57% in USA
Fukushima Daiichi nuclear disaster (2011)
Chernobyl disaster (1986)
Three Mile Island accident (1979)
The Stationary Low-Power Reactor Number One (SL-1) is United States Army experimental nuclear power reactor which underwent a steam explosion and meltdown on January 3, 1961, killing its three operators (Idaho Falls).
Image: http://en.wikipedia.org/wiki/File:US_AEC_SL-1.JPG

## Slide 54: Nuclear reactor fallout
Three Mile Island, near Harrisburg, PA, 1979.
  Partial meltdown of unit 2. No direct deaths.
  Voluntary evacuations, some release of radioisotopes (ca. 43,000Ci of 85Kr, <20Ci 131I (8 day half-life))*
  Unit 1 produces about 800MW today.
Chernobyl, near Kiev, Ukraine, 1986.
  Explosions expose graphite moderator, which ignites.
  Core may have vaporized?
  350,400 evacuated, land
  50 million - 30 billion curies estimated released.
* Curie = 37 billion counts per second

## Slide 55: Nuclear reactor fallout
SL1 (1961)
  The direct cause was the improper withdrawal of the central control rod, responsible for absorbing neutrons in the reactor core. The incident released about 80 curies (3.0 TBq) of iodine-131, which was not considered significant due to its location in a remote desert of Idaho. About 1,100 curies (41 TBq) of fission products were released into the atmosphere.
Fukushima Daiichi nuclear disaster
  was a catastrophic failure at the Fukushima Nuclear Power Plant on 11 March 2011, resulting in a meltdown of three of the plant's six nuclear reactors

## Slide 56: Nuclear reactor issues: Waste
Since only about 0.1% of the mass is converted to energy in nuclear fission, 99.9% of the mass of the fuel is converted to waste. Includes radio-toxins, chemically toxic elements.
Also contaminated by fission are:
control rod material
fuel rod material
cooling water (deuterium, tritium). Both can be used as fusion fuel.
containment structure material that absorbs neutrons.
Radioactive material will continue to decay, releasing energy. Heat buildup must be prevented.

## Slide 57: New material
Nuclear fission splits a heavy nucleus such as uranium or plutonium into two lighter nuclei, which are called fission products.
Yield refers to the fraction of a fission product produced per fission.
Ma: million years:1×106
Years.
http://upload.wikimedia.org/wikipedia/en/thumb/4/44/Fission_yield_volatile.png/450px-Fission_yield_volatile.png
Prop: Unit: | t½ Ma | Yield % | Q * KeV | βγ *
99Tc | 0.211 | 6.1385 | 294 | β
126Sn | 0.230 | 0.1084 | 4050 | βγ
79Se | 0.327 | 0.0447 | 151 | β
93Zr | 1.53 | 5.4575 | 91 | βγ
135Cs | 2.3 | 6.9110 | 269 | β
107Pd | 6.5 | 1.2499 | 33 | β
129I | 15.7 | 0.8410 | 194 | βγ

## Slide 58: Results of 235U fission
Many emit neutrons (danger!)
Iodine, cesium, e.g. are chemically absorbed by body.
Short lifetime  high decay rate, but are dangers for shorter periods of time.
    133Cs “hotter”, but 137Cs can stay in body longer (melts at 28 ᵒC and reacts with water).
    133Cs is used in electronics, 137Cs is used in medical applications
Table: http://en.wikipedia.org/wiki/Fission_product_yield

## Slide 59: Units of radiation
Rate of decay (Decay does not depend on the history of the elements, and 2 isotopes do not have the same time of decay)
  Becquerel = 1 decay / sec
  Ignores differences between alphas, betas, gammas, the energy of the radiation, the mass of the tissue in which it is deposited.
Absorbed dose = energy deposited per mass of tissue
Absorbed dose = energy / mass.
rad = radiation absorbed dose = 0.01J/kg
  rad = radiation absorbed dose = 0.01J/kg
  gray (Gy)=1J/kg=100rad
Equivalent dose
  Impact depends on type of tissue, too

## Slide 60: Biological Effects of Radiation
Effect depends on
  Kind of radiation
  Duration of exposure
  How much is adsorbed
  Kind of tissue exposed
Ionizing radiation
nucleus
Valance electron
nucleus
Becomes more chemically active
http://www.biologycorner.com/bio1/cell.html

## Slide 61: Exposure to Radiation
Natural sources = 0.3 rem (roentgen equivalent in man, 1rem=1 rad )
  0.2 rem inhaled from radon
  0.07 rem from food/water due to soil and building materials
  0.03 rem from cosmic radiation
Human Activity = up to 0.3 rem
  medical and dental diagnostic treatment (x-rays)
http://www.homeprocanada.ca/radon/HP_radon.htm

## Slide 62: Penetration of Radiation
  Alpha
  • Range in human tissue 0.03-0.33 mm
  (can be stopped by paper)
  • Can’t penetrate the skin, so outside of the body they are not dangerous
  • Inside of the body, they are the most dangerous because they can ionize large numbers of molecules. They lose their energy through a large number of collisions with molecules.
  • Alpha emitters present in food can deliver significant radiation to the digestive track and other body tissue
Paper aluminum concrete/lead

## Slide 63: Penetration of Radiation
  Beta, electron
  •Range in human tissue is a few cm
  •They can ionize molecules, and as they are slowed down, they emit X-rays. They lose their energy as they collide with molecules.
  •More dangerous inside the human body than outside (but not as dramatic difference as )
  Gamma, EM radiation)
  •They can lose all of their energy in a single interaction.
  • gamma irradiated milk
  •cancer radiation therapy
Paper aluminum concrete/lead

## Slide 64: Common sources of radiation
http://www.stopcancerfund.org/wp/wp-content/uploads/2010/02/table-radiation-dose-and-risk.bmp,

## Slide 65: Nuclear waste
The largest amount of radioactive waste in the US comes mostly from military defense program.
These wastes are ( about 80 millions gallons) are stored in large underground tanks at Hanford (Washington), and Savannah River ( South Carolina).
Some in Hanford developed leaks in earlier years (500,000 gallons) and the leaks were discharged into the ground contaminating 100 square miles with no known human casualties.

## Slide 66: Nuclear waste
Nuclear Act Policy of 1982 and its Amendment Act of 1987 established a policy for the management of nuclear waste.
In 1987, the Yucca Mountain , Nevada location was selected by the US congress as the nuclear repository site.
It took several years to study the Yucca mountain, and a cost of $6 billion.
The study focused on earthquakes, volcanoes , water movement through the rock and so on.
The study discovered that The Yucca Mountain site consists of “tuff”: a dense form of volcanic ash produced more than 13 million years ago.
In 2009 , the site was removed from the list of possible nuclear waste repositories.

## Slide 67: Nuclear waste
Nuclear waste requires sophisticated treatment and management to successfully isolate it from interacting with the biosphere.
It necessitates treatment, followed by a long-term management strategy involving storage, disposal or transformation of the waste into a non-toxic form.
Governments around the world are considering a range of waste management and disposal options, though there has been limited progress toward long-term waste management solutions

## Slide 68: Nuclear Waste
In second half of 20th century, several methods of disposal of radioactive waste were investigated by nuclear nations:
"Long term above ground storage", not implemented.
"Disposal in outer space", not implemented.
"Deep borehole disposal", not implemented.
"Rock-melting", not implemented in the US.
"Disposal at subduction zones", not implemented.

## Slide 69: Nuclear Waste
And
"Ocean disposal", done by the USSR, the United Kingdom, Switzerland, the United States, Belgium, France, The Netherlands, Japan, Sweden, Russia, Germany, Italy and South Korea. (1954–93): this is no longer permitted by international agreements.
"Sub seabed disposal", not implemented, not permitted by international agreements.( a close tank that you plunge in the ocean)
"Disposal in ice sheets", rejected in Antarctic Treaty
"Direct injection", done by USSR and USA.

## Slide 70: Ocean disposal of radioactive waste
From 1946 through 1993, thirteen countries used ocean disposal or ocean dumping as a method to dispose of nuclear/radioactive waste.
Since 1993, ocean disposal has been banned by international treaties.
Some companies have been dumping radioactive waste and other hazardous materials into the coastal waters of Somalia, taking advantage of the fact that the country had no functioning government from the early 1990s onwards.
According to the United Nations, this caused health problems for locals in the coastal region and posed a significant danger to Somalia's fishing industry and local marine life.

## Slide 71: Other Methods of Disposal
Direct injection includes injection of liquid radioactive waste directly into a layer of rock very deep underground. This concept has been practiced by Russia and the US.
Rock melting: the melting of waste is done in the adjacent rock. The main point is to produce immobilized mass of waste. This technique is reserved exclusively for heat-generated waste.

## Slide 72: Direct Injection
Injection of liquid radioactive waste directly into a layer of rock deep underground.
Layer of rock (injection layer) with sufficient porosity to accommodate the waste and with sufficient permeability to allow easy injection (i.e. act like a sponge).
Above and below the injection layer there must be impermeable layers that act as a natural seal.
Example: injection into layers of rock containing natural brine groundwater. This is because the high density of brine (salt water) would reduce the potential for upward movement.

## Slide 73: Critical Mass
A critical mass is the smallest amount of fissile material needed for a sustained nuclear chain reaction.
The critical mass of a fissionable material depends upon its nuclear properties: (specifically, the nuclear fission cross-section), density, shape, enrichment, purity, temperature, and surroundings.
Critical mass is important in nuclear weapon design.

## Slide 74: Critical mass
Top: A sphere of fissile material is too small to allow the chain reaction to become self-sustaining as neutrons generated by fissions can too easily escape. Middle: By increasing the mass of the sphere to a critical mass, the reaction can become self-sustaining. Bottom: Surrounding the original sphere with a neutron reflector increases the efficiency of the reactions and also allows the reaction to become self-sustaining.
If two pieces of subcritical material are not brought together fast enough, nuclear predetonation (fizzle) can occur, whereby a very small explosion will blow the bulk of the material apart.
Images: http://en.wikipedia.org/wiki/Critical_mass

## Slide 75: Criticality accident
A criticality accident is an uncontrolled nuclear chain reaction.
It is sometimes referred to as a critical excursion or a critical power excursion and represents the unintentional assembly of a critical mass of a given fissile material, such as enriched uranium or plutonium, in an unprotected environment.
At least sixty criticality accidents have been recorded since 1945. These have caused at least twenty-one deaths: seven in the United States, ten in the Soviet Union, two in Japan, one in Argentina, and one in Yugoslavia. Nine have been due to process accidents, and the others from research reactor accidents.

## Slide 76: Critical mass: oopsies!
21 deaths since 1945 in 60 “criticality accidents”.
Left: As part of a re-creation of a 1945 criticality accident, a plutonium pit is surrounded by blocks of neutron-reflective tungsten carbide. The original experiment was designed to measure the radiation produced when an extra block was added. Instead, the mass went supercritical.
Right: A re-creation of the Slot in incident from the film “Fat Man and Little Boy”. The inside hemisphere next to the hand is beryllium, with an external larger tamper under it, of natural uranium. The 3.5-inch-diameter (89 mm) plutonium "demon core" (the same as in the Daghlian incident) was inside, and is not visible.
Images: http://en.wikipedia.org/wiki/Critical_mass