## Slide 1: Lecture 7
Analysis of Proteins

## Slide 2
Protein - Characterization
Absorbance Spectroscopy: The aromatic amino acids all have characteristic absorbance profiles
5500 M-1cm-1
1490 M-1cm-1
Also Cysteine
125 M-1cm-1
ExPASy Tool: ProtParam http://web.expasy.org/protparam/

## Slide 3
Protein Characterization
Electrophoresis: separation of polar compounds based on their
mobility through a solid support. The separation is based on
charge (pI – Isoelectric Focusing) or molecular mass (SDS-PAGE).

## Slide 4
Protein Characterization
Electrophoresis: separation of polar compounds based on their
mobility through a solid support. The separation is based on
charge (pI – Isoelectric Focusing) or molecular mass (SDS-PAGE).

## Slide 5
Protein Characterization
2D Electrophoresis:
Isoelectric Focusing
SDS-PAGE
How could this be useful?

## Slide 6
Protein Characterization
Ultracentrifugation: Technique that was developed to separate proteins by mass.
Relies on ultra high centrifugation speeds (80,000 RPM)
Big molecules sediment more slowly than small molecules
Native Protein Structure
Data measured in Svedberg Units (S)
Size vs. S is NOT linear!

## Slide 7
Protein Characterization
Ultracentrifugation: Technique that was developed to separate proteins by mass.

## Slide 8
Protein Characterization
peptide
-or-
protein
[H]
reduce any
disulfide
bonds
individual
amino acids
H3O+, 
1972 Nobel Prize in Chemistry
William Stein
Stanford Moore
liquid
chromatography
derivatize w/
ninhydrin
Detected w/
UV-vis
Different amino
acids have different
chromatographic
mobilities (retention
times)
Amino Acid Analysis: Determine the total amino acid content within a protein

## Slide 9
Sequencing from the N-terminus
Edman Degradation
H+
What analytical techniques would be useful to identify the PTH amino acid?
PVDF membrane
Phenyl Thiazoline

## Slide 10
Sequencing Complications
Edman degradation is limited to ~40-60 amino acids
Incomplete reactions
Side reactions
Peptide loss
Method 2 Specificity
Method 1 Specificity

## Slide 11
Peptide Cleavage Reactions – Cyanogen Bromide
H2O
g carbon becomes electrophilic
Cyanogen bromide cleaves C-term to ALL methionines

## Slide 12
Sequencing Complications
ExPASy Tool: Peptide Cutter http://web.expasy.org/peptide_cutter/

## Slide 13
Sequencing Summary
What are these and why are they used?

## Slide 14
Sequencing Summary
MEGVNDNEEMGFFSAR
Peptide 1
Peptide 2
Endopeptidase Treatment
FWMGAK
Peptide 3
ALAPP
Peptide 4
VHLTPEEK
GAKALAPP
CNBr treatment
GFFSARVHLTPEEKFWM
Peptide 2
Peptide 1
Peptide 3
EGVNDNEEM
GFFSARVHLTPEEKFWM
FWMGAK
VHLTPEEK
GAKALAPP
MEGVNDNEEMGFFSAR
ALAPP
EGVNDNEEM

## Slide 15: Mass Spectrometry

## Slide 16: Soft Ionization Techniques
Electrospray Ionization (ESI)
Aqueous sample introduced to metal capillary
High voltage (2000-4000 V) applied
Released to vacuum
Desolvation of aerosol leaving highly charged ions
Matrix Assisted Laser Desorption Ionization (MALDI)
Aqueous sample is cocrystallized on a metal surface with a Matrix
Intense Laser beam is directed toward sample/matrix mixture - desorption
Matrix absorbs the energy and is ionized
Some of the charge is transferred to the analyte

## Slide 17: MALDI Matrix
α-cyano-4-hydroxycinnamic acid (CCA)
2,6-dihydroxyacetophenone (DHAP)
Sinapinic Acid (SA)

## Slide 18: Separation Techniques
Flight Tube
Quadrupole
Four rods are arranged opposite each other and connected electronically
Voltage applied to each rod is carefully regulated
The trajectory of a charged particle is influenced by the electric field
Molecules separate by the time it takes for them to travel from the ion source to the detector
Resolution is dependent on tube length (limits resolving power)
Reflectron enhances the resolution

## Slide 19: Ideal Pairs
ESI-QMS
MALDI-TOF MS

## Slide 20
ESI-QMS Spectrum
What is the parent mass?

## Slide 21
ESI-QMS Spectrum
1415.68
1375.232
1337.032
1300.896
1266.661
1234.183
1203.328
1173.979
1146.027
1119.375
1093.935
1069.625
1046.373
1024.109
What is the parent mass?

## Slide 22
Mass Spec and Sequencing

## Slide 23
Mass Spec and Sequencing

## Slide 24
Structural Predictions – Chou Fasman
Guidelines
A cluster of 4 helix forming residues (Ha or ha) out of 5 sequential residues will nucleate a helix.
  Once the average value of 4 sequential residues falls below 1, the helix is broken.
A cluster of 3 sheet forming residues (Hb or hb) out of 5 sequential residues will nucleate a sheet.
  Once the average value of 4 sequential residues falls below 1, the helix is broken.
If both helix and sheet are predicted, the highest average value will be preferred.
http://www.biogem.org/tool/chou-fasman/

## Slide 25
AA | Helix |  | Sheet | 
Gln | 1.11 | h | 1.10 | h
Leu | 1.21 | H | 1.30 | h
Met | 1.45 | H | 1.05 | h
Thr | 0.83 | i | 1.19 | h
Trp | 1.08 | h | 1.37 | h
Ala | 1.42 | H | 0.83 | i
Ser | 0.77 | i | 0.75 | b
Thr | 0.83 | i | 1.19 | h
Pro | 0.57 | B | 0.55 | B
Cys | 0.70 | i | 1.19 | h
Gln Leu Met Thr Trp Ala Ser Thr Pro Cys
Structural Predictions – Chou Fasman

## Slide 26
Structural Predictions – Chou Fasman

## Slide 27
Peptide Synthesis
Fmoc
Activated Ester

## Slide 28
Peptide Synthesis

## Slide 29
Peptide Synthesis