## Slide 1: Geothermal Power
Dr. Harris
Phys 105
4/3/13

## Slide 2: What is Geothermal Energy?
Geothermal energy is defined as heat from the Earth. It is a clean, renewable resource that provides energy around the world.
It is considered a renewable resource because the heat emanating from the interior of the Earth is essentially limitless.
Geothermal is a natural form of nuclear power, as it originates from radioactive decay.

## Slide 3: Origin of Geothermal Power
Crust
Upper Mantle
Mantle
Outer Core
Inner Core
600oC
1200oC
4000oC
5000oC
Geothermal energy originates from the Earth’s core, which is estimated to have a temperature of about 5,000° C. This nearly constant temperature is possible because of continuous radioactive decay, compression, and because the core is very well insulated.

## Slide 4: Harnessing Geothermal
Geothermal power emits from earth at a rate of 44 x 1012 W. This is more than double the total power consumption of the world.
The Earth’s crust acts as a massive insulating “blanket” that traps this heat deep under the surface. Thus, the crust must be pierced to release this heat
Unfortunately, this power is too spread out to effectively use it all.
The distribution of geothermal energy, however, is not uniform. Certain regions have an enormous geothermal resource
    Where the crust is thin or fractured, as at the edges of tectonic plates, volcanoes, geysers and hot springs deliver this energy to the surface.

## Slide 5: Geothermal Sources
Hot Water Reservoirs
  Heated underground water pools, very large in magnitude in the U.S.; not appropriate for electricity but can be useful for space heating
Natural Steam Reservoirs*
  e.g. The Geysers power plant (Ca). Highly desirable type of resource for direct generation of electric, though very rare
Geopressured Reservoirs*
  Hot, superheated brine solution saturated with natural gas. Useful for both its heat content and natural gas
Hot Dry Rock
  Hot rock can be used to heat a working fluid is forced through a series of man-made channels and cycled. No technology yet exists to do this
Hot Molten Rock (Lava)
  No technology yet exists to extract heat energy from lava

## Slide 6: Estimated U.S. Geothermal Resources
Resource Type | Total Resource (QBtu) | Potentially Usable Resource (QBtu)
Hot Water | 12,000 | 6,000
Natural Steam | 180 | 45
Geopressurized | 73,000 | 2,400
Hot Rock | 1,410,000 | 14,100
Lava | 3,500 | 35
* The U.S. consumes 98 QBtu of energy per year

## Slide 7: Geothermal Power Plants
There are three types of geothermal power plants
  Direct Dry Steam Plants
  Flash Cycle Plants
  Binary Closed Cycle Plants

## Slide 8: Direct Dry Steam Power Plant

## Slide 9: The Geysers (California)

## Slide 10: Flash Cycle Plants
Uses superheated brine. When the brine enters a low pressure chamber called a flash tank, it instantly vaporizes (flashes).

## Slide 11: Binary Closed Cycle Plants
Binary closed cycle plants use a working fluid (i.e. Freon) to spin a turbine. The working fluid cycles through a heat exchanger where it is evaporated by hot water from a geothermal reservoir.
evaporator
condenser
hot water
flow direction
working fluid
Cold water
pump

## Slide 12: Binary Closed Cycle Turbine At Chena Power Plant in Alaska

## Slide 13: Binary Closed Cycle Plants
Binary cycle plants are the most useful because it is not necessary for the water to reach the extreme temperatures that are experienced with dry steam and flash plants.
  The water in a binary cycle plants needs only to be above the boiling temperature of the working fluid
Considering that most geothermal water is of moderate temperature (> 400oF), these are the most useful and most viable types of geothermal plants.

## Slide 14: Advantages of Geothermal
Geothermal energy is a renewable energy source.
Geothermal energy is relatively clean
  Produces 12% of GHG emission of fossil fuel plants)
Geothermal energy can be used for cooling and heating homes.
Not subject to the same fluctuations as solar or wind
Smallest land footprint of any major power source
Virtually limitless supply
Inherently simple and reliable
Can provide base load or peak power
Already cost competitive in some areas (~$0.07 per kWh)
Could be built underground
Massive potential for the utilization of untapped sources
New technologies show promise to utilize lower water temperatures

## Slide 15: Disadvantages of Geothermal
High upfront costs associated with exploration and drilling
Finite lifetime of useful energy production
  Continuous drop in thermal output overtime
  Once the thermal energy of a well is tapped, it requires a “recharging” period that can take several years.
Very location specific (e.g. Iceland)
There are significant volumes of greenhouse gases and toxic compounds such as hydrogen sulfide that are released when geothermal reservoirs are tapped
  Foul smelling gases
  Pumps used to circulate working fluid consume fossil fuel
Earthquakes induced by fracking.