## Slide 1: Atomic Bonding
https://www.youtube.com/watch?v=jBSHhtzZeSA
Primary Bonding:
Ionic Bonding, non-directional
Metallic Bonding, non-directional
Covalent Bonding: strong, localized, and directional
Secondary Bonding (or Van der Waals bonding):
Induced dipole/induced dipole
Permanent/induced dipole
Permanent/Permanent dipole
Hydrogen bonding

## Slide 2: Metallic Crystal Structures
• Tend to be densely packed.
• Reasons for dense packing:
- Typically, only one element is present, so all atomic
radii are the same.
- Metallic bonding is not directional.
- Nearest neighbor distances tend to be small in
order to lower bond energy.
- Electron cloud shields cores from each other
• Have the simplest crystal structures.
We will examine three such structures...

## Slide 3: table_03_01
Visit this vernier web site and learn how to use a vernier caliper. http://www.youtube.com/watch?v=4hlNi0jdoeQ

## Slide 4: Simple Cubic Structure (SC)
• Rare due to low packing density (only Po has this structure)
• Close-packed directions are cube edges.
Click once on image to start animation
(Courtesy P.M. Anderson)
Adapted from Fig. 3.24,
Callister & Rethwisch 8e.
close-packed directions
a
R=0.5a
contains 8 x 1/8 =
1
atom/unit cell

## Slide 5: Body Centered Cubic Structure (BCC)
• Coordination # = 8
Adapted from Fig. 3.2,
Callister & Rethwisch 8e.
• Atoms touch each other along cube diagonals.
--Note: All atoms are identical; the center atom is shaded
differently only for ease of viewing.
ex: Cr, W, Fe (), Tantalum, Molybdenum
2 atoms/unit cell: 1 center + 8 corners x 1/8
Click once on image to start animation
(Courtesy P.M. Anderson)
https://www.youtube.com/watch?v=CsnNbuqxGTk

## Slide 6: Density: BCC
a
length = 4R =
Close-packed directions:
3 a
a
R
Adapted from
Fig. 3.2(a), Callister & Rethwisch 8e.
a
2
a
3

## Slide 7: Face Centered Cubic Structure (FCC)
• Coordination # = 12
Adapted from Fig. 3.1, Callister & Rethwisch 8e.
• Atoms touch each other along face diagonals.
--Note: All atoms are identical; the face-centered atoms are shaded
differently only for ease of viewing.
ex: Al, Cu, Au, Pb, Ni, Pt, Ag
4 atoms/unit cell: 6 face x 1/2 + 8 corners x 1/8
Click once on image to start animation
(Courtesy P.M. Anderson)

## Slide 8: Density: FCC
Close-packed directions:
length = 4R =
2 a
Unit cell contains:
6 x 1/2 + 8 x 1/8
=
4 atoms/unit cell
Adapted from
Fig. 3.1(a),
Callister & Rethwisch 8e.