Hooke’s Law                            Name:_________________

Purpose: To investigate Hooke’s law and determine the spring constants of elastic springs.

Apparatus: Springs, mass set, mass hanger (small), pendulum clamp, lab stand, and meter stick.

Theory: Think about stretching a spring. The more stretching force you apply, the more stretch you get. Robert Hooke (1635-1703), a British physicist, discovered this empirical relationship between the stretching force (F) and the stretch (x), known as Hooke's law.

|  | The stretching force is provided by the added mass. Stretching Force = (Spring constant) X Stretch. Spring constant = k = (Stretching Force)/Stretch. When you collect data make sure that you reach the maximum stretch on the scale. Hooke’s law is verified when there is a linear relationship between Added mass & Stretch. |
| --- | --- |

Procedure: Attach the mass hanger to the hard spring and hang the spring from the pendulum clamp. Attach the meter stick so that the 0-cm is at the bottom of the mass hanger. Add the mass and measure the stretch. Repeat this for other masses and then for other springs.

DATA

For the Hard spring, start with an added mass of 100-g and increase it by 100-g thereafter.

| Hard Spring | Medium Spring | Light Spring |
| --- | --- | --- |
| Added Mass(g) | Stretch (cm) | Added Mass(g) | Stretch (cm) | Added Mass(g) | Stretch (cm) |

DATA ANALYSIS

Enter the above data in a spread sheet program and create three more columns for each spring; Stretch in meter, Stretching Force in newton, and Spring Constant in N/m. Plot Stretching Force versus Stretch and determine the slope, which is the average spring constant. Display the plots for the three springs in the same graph.

Attach your hard copies of the data table and graph and then attach your conclusion page.

Include the following in your conclusion:

- Begin your conclusion by re-stating the purpose in an appropriate form.

- For each spring, state whether Hooke's law is verified or not.

- For each spring, comment about how the spring constant changes as the stretching        force & stretch increases.

- List the average values of the spring constants you determined from the plots.

- List the sources for errors and suggestions for improvements.